## Slide 1: #3 How to create a basic Bluetooth® Low Energy peripheral in 10 min Click & Go

## Slide 2: Prerequisites Refresh
  STM32CubeWBA MCU package (v1.2.0 as basis + optional patch)
  IDE: STM32CubeIDE (1.14.0)
  A serial terminal (e.g. TeraTerm)
  ST BLE ToolBox Smartphone application
  NUCLEO-WBA52
  USB C cable
ST BLE Toolbox
SW prerequisites
HW prerequisites
NUCLEO STM32WBA55

## Slide 3: Basic Peripheral in 10mn : Click & Go :

## Slide 4: Purpose
As a first exercise, Let’s start from an existing project example BLE_P2PServer
Purpose of this session is to modify this code example to customize advertising data (Local name).
In the second part of the Hands on we will generate associated code, flash and test over Nucleo-WBA5x board
BLE_P2PServer Application
STM32WBA55
BLE_P2PServer
+

## Slide 5
GATT Client
GATT Server
ST BLE Toolbox
What is a P2P Server?
GAP central
GAP peripheral
P2P is a Generic Attribute Profile (GATT) based on Bluetooth® Low Energy defined by STM with proprietary UUIDs 128bit
Notes: What are we going to do?
Create device that can report values to mobile phone and accept commands from it
Example use cases: Thermostat, or any other home appliance with some sensor and some actuator
How are we going to do that? We will start from empty CubeMX project and add all peripherilas that BLE Middleware rely on. Then we will add some application code for sending and receiving data.

## Slide 6
GATT Client
GATT Server
ST BLE Toolbox
What is a P2P Server?
GAP central
GAP peripheral
P2P is widely used for direct connection and defined connection between GATT Server and GATT Client
Write - LED
Notification - SWITCH
Notes: What are we going to do?
Create device that can report values to mobile phone and accept commands from it
Example use cases: Thermostat, or any other home appliance with some sensor and some actuator
How are we going to do that? We will start from empty CubeMX project and add all peripherilas that BLE Middleware rely on. Then we will add some application code for sending and receiving data.

## Slide 7: STM32Cube capabilities
STM32Cube allow to start design within 3 options
Example application
complete application running over NUCLEO
1
Board level
    all the hardware is already configured (NUCLEO_WBA55)
2
Chipset level
    require to configure your HW (PCB) & your application
3
7
+

## Slide 8: Connect the NUCLEO-WBA55CG to the PC
3 user LEDs
3 user buttons
STLINK-V3MODS
Programming
Debugging
VCOM
STM32WBA55CG
+

## Slide 9: START STM32CubeIDE Open BLE_P2PServer example
1
2
3

## Slide 10: START STM32CubeIDE Open BLE_P2PServer example
At this stage, Default BLE_P2PServer project source code is ready to be modified, built and flash using STM32CubeIDE
1

## Slide 11: Let’s customize this BLE_p2pServer
Double click on .ioc file to Open CubeMx graphical interface
1

## Slide 12: Customize Local Name
1
2
3
4
Local Name must be < 11
CubeMx contraints

## Slide 13: Customize Device Name
1
2
3
4
set same Device name =
Local Name
iOS displays Local Name (advertising data) prior to a 1st connexion.
After a 1st connexion iOS displays Device name (thanks to look up table : associates BLE MAC @ & Device Name)

## Slide 14: Code Generation
1

## Slide 15: Build and flash modified project
1
Build
2
Flash
3
Plug the board

## Slide 16: Enjoy your first STM32WBA55 project running!
ST BLE Toolbox

## Slide 17: STBLE Toolbox
1
click on device
2
click on connect

## Slide 18: STBLE Toolbox
3
access to profile
4
control LED status on Nucleo

## Slide 19: STBLE Toolbox
5
push button 1 and notify device
6
click on details to see bytes sent/received

## Slide 20: What’s next ?
start and build from turn-key server application
    start from chipset, initialize and configure BLE server application
completed
#1
initialize your HW
#2
configure & understand BLE settings (Adv, service, characteristic)
#2
modify application code & build
client
Server
Send alert
Control LED

## Slide 21
Find out more at www.st.com
You can personalize this
last page with a short link
(ex. www.st.com/shortlink)
You can find a complete list of st.com short links on this page:
http://seo.st.com/toolbox/shortcuts/

## Slide 22
For further support in creating a PowerPoint presentation, including graphic assets, formatting tools and additional information on the ST brand
you can visit the ST Brand Portal https://brandportal.st.com
Please remove this page
before publishing the
presentation